Cochlear Micro-structures: From Mechanics to Neuroscience

Prof.  Yong-Jin Yoon

尹勇軫 博士

School of Mechanical & Aerospace Engineering,

Nanyang Technological University,Singapore

新加坡南洋理工大學 機械與宇航工程學院

Abstract

The cochlear physiologies of four species, gerbil, chinchilla, cat, and human, are simulated with a three-dimensional hydro-dynamic cochlear model with “feed-forward and feed-backward” active mechanism for the organ of Corti and solution calculated using a “time-averaged Lagrangian”. The basilar membrane velocity (VBM) results for the gerbil and chinchilla cochlea show reasonable agreement with the physiological measurements (Ren and Nuttall, 2001; Ruggero et al., 1997; Dong and Olson 2005). Interspecies BM velocity (3.7-164 um/sdepending on species) and displacement (0.1-3.3 nm) thresholds are estimated by equating the simulation results to neural thresholds at the best frequency (BF).

The Q10 (BF/bandwidth-10dB-down) for the measurements increase smoothly and monotonically with frequency, whereas for the model calculations the curves increase monotonically with curvature. The model calculations are for a single prototypical representation of a given species and thus there is no averaging across animals. Parameters that control the tuning include the OHC gain factor and angle relative to the deiters cell and the reticular lamina and the phalangeal process angle and possibly the width of the basilar membrane.

Speaker Bio

Dr. Yong-Jin Yoon joined Department of Mechanical and Aerospace Engineering at Nanyang Technological University (NTU) as an Assistant Professor in January, 2010. He obtained his Ph.D. degree in the Mechanical Engineering at Stanford University in September 2009. During his PhD study, he also obtained two Master degrees in Stanford: one in Electrical Engineering, focusing on MEMS and Signal Processing, and the other in Mechanical Engineering, focusing on Medical Device Design. He was the co-founder of one internet solution company and one online game company in South Korea back in year 2000.

During his doctoral study in Stanford, he worked in OtoBiomechanics Group in the fields of hearing mechanics. He worked closely with Stanford Medical School Otolaryngology Department for Head, Neck Surgery, focusing on inner- and middle-ear biomechanics, auditory technologies, surgical simulations, μCT and MR imaging.   Currently, his researches at NTU include biomimetic electroacoustic MEMS transducer, psychoacoustic neuroscience, bio-chemical MEMS sensor, medical device, and surgical simulation.  Contact: yongjiny@ntu.edu.sg